## Slide 1: CSC4780 – Network security
Instructor: Susmit Shannigrahi
sshannigrahi@tntech.edu

## Slide 2: Chapter 1: Fundamentals
Networking is ubiquitous
  (Breakout) What did you use it for today?
First things first:
  Terminology
  Basic tools
  What does it take to build an Internet?
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 3: Links, Nodes, Network, Internet
You can view the network as a graph
Each device (a phone, a computer) is a node
Each connection is a link
  Wires = real links
  Bluetooth, Radio, Infrared = virtual links
Nodes + links = a network
  Many connected networks = Internet
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 4: Links, Nodes, Cloud, Routers, Switches
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 5: A Network and the Internet
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 6: Network Architecture
What are the requirements from a network?
Architecture = High-level blueprint
  Protocols = Building blocks of the architecture
  Layering = Break down the problem in smaller pieces

## Slide 7: Network Layers
Makes it easier to divide functionality
Hides implementation details
Breakout – few other reasons?
Export Service
Use Service

## Slide 8: IP Suite
wikipedia
We reject kings, presidents, and voting. We believe in rough consensus
and running code. (David Clark, IETF, July 1992)

## Slide 9: TCP/IP Layers
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Ethernet Interface
Ethernet Interface
Segments
Data
Packets
Frames
Bits (1010001)

## Slide 10: What does it take to create a link?
Common abstractions
  Why?

## Slide 11: Packet to Low level Signals
Bit pattern - 0101001
  Must encode it into electrical signals and then decode it on the other end!

## Slide 12: Frames – bag of bits
Bits - between adaptors
Frames – between hosts (two computers)
  The job of adaptors is to find frames in a bit sequence
Frames are link layer protocols
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 13: Requirements:   Packet framing: encapsulation of network-layer datagram in data link frame   Bit transparency: Does not care about what its carrying   Error Detection: Correction is on upper layers   Connection liveness   Network layer address negotiation
Point to Point Links
Notes: The University of Adelaide, School of Computer Science
24 January 2026
Chapter 2 — Instructions: Language of the Computer
13

## Slide 14: Reliable Delivery
Frames might get lost
  Too many bits lost
  Clock did not sync properly
  Error detected but the report got lost
Can we build links that does not have errors?
  Not possible
How about all those error correction stuff we learned?
  Can we add them to frames?
  We could, but think of the overhead
  What happens when the entire frame is lost?
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 15: Stop and Wait
Sender sends a frame, sets a timeout (e.g., 1 sec)
Receiver receives the frame,
sends an ACK
Sender
  sends the next frame on ACK
  retransmits the same frame if timeout happens
If I had to attack this protocol, how would I do it?
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 16: Ethernet – Wire as Shared Medium
We created a frame – how to use it for communication?
Most successful local area networking technology of last 20 years.
Developed in the mid-1970s by researchers at the Xerox Palo Alto Research Centers (PARC).
For alohanet the medium was the atmosphere, for ethernet, coax cables
Frames
Frames
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 17: Ethernet
Ethernet repeater
Notes: The University of Adelaide, School of Computer Science
24 January 2026
Chapter 2 — Instructions: Language of the Computer
17

## Slide 18: Ethernet – Random Access
How to allow many adaptors to send frames over the wire?
  Random access
  When you have data – send at Full channel rate!
  No coordination needed.
If collision happens
  Detect
  Recover
  Retransmit
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 19: Ethernet Frame
SYNC- 7 bytes of 10101010 1 byte of 10101011
MAC ADDRESSES
Upper layer protocol
(usually IP)
Payload
Notes: The University of Adelaide, School of Computer Science
24 January 2026
Chapter 2 — Instructions: Language of the Computer
19

## Slide 20: Wireless Links
A wireless network using a base station
Typically connects to
Base stations Multiple access Handoff protocols
Wireless != Mobile

## Slide 21: Wireless Links – problems and attacks?
A
B
C
A and C can talk
B and C can talk
A and B can not!!! Interference at B
Hidden terminal
Signal Fading
space
A
B
C
A’s signal
strength
C’s signal
strength
Notes: The University of Adelaide, School of Computer Science
24 January 2026
Chapter 2 — Instructions: Language of the Computer
21

## Slide 22: TCP/IP Layers
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Ethernet Interface
Ethernet Interface
Segments
Data
Packets
Frames
Bits (1010001)

## Slide 23: Switching
Switch
  A mechanism to interconnect
  links to form a large network
  Forward frames
  Separate the collision domains
  Filter packets between LANs
  Connects two or more LAN segments - Bridging
LAN 1
Collision domain 1
LAN 2
Collision domain 2
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 24: Switching Table
To decide how to forward a packet, a switch consults a forwarding table
Destination, Port
-------------------------------------
A 3
B 0
C 3
D 3
E 2
F 1
G 0
H 0
Forwarding Table for Switch 2
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 25: Internet Protocol (IP)
    What is an internetwork?
    An arbitrary collection of networks interconnected to provide some sort of host-host to packet delivery service
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 26: Global Address in IP – Each node has an unique address
    A 32 bit number in quad-dot notation
    Identifies an Interface
    A host might have several interfaces!!!
    129.82.138.254
    10000001.01010010.10001010.11111110
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 27: IP addresses are in Network + Host
    1.1.2.1 →
    1.1 → Network part
    2.1 → host part
    Each octet can range from 1- 255
    Hierarchical address
5.1.6.7
1.1.*.* | Interface 3
1.1.2.2
1.1.2.1
129.82.138.254 10000001.01010010.10001010.11111110
Network part (24 bits). Host part(8 bits)
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 28: You have an address – Send data now. Problems?
    Packet Delivery Model
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 29: IP Packet
Version (4): 4
Hlen (4): number of 32-bit words in header
TOS (8): type of service (not widely used)
Length (16): number of bytes in this datagram
Ident (16): used by fragmentation
Flags/Offset (16): used by fragmentation
TTL (8): number of hops this datagram has traveled
Protocol (8): demux key (TCP=6, UDP=17)
Checksum (16): of the header only
DestAddr & SrcAddr (32)
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 30: IP Routing
Forwarding:
          to select an output port based on destination address and routing table
          Local path
    Routing:
          process by which routing table is built
          End-to-end path
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 31: Interdomain Routing
IGP
Interior gateway protocol
A network with four autonomous systems
IGP
Interior gateway protocol
IGP
Interior gateway protocol
IGP
Interior gateway protocol
BGP
Border gateway protocol

## Slide 32: BGP: Path vector protocol
AS 223
AS 225
AS 245
AS 7770
Path: AS 223
Path: AS 223, AS 225
Path: AS 223, AS 225, AS 245
Path: AS 223, AS 225, AS 245, AS 7770
Path: AS 223, AS 225, AS 245, AS 7770
Loop!

## Slide 33: TCP/IP Layers
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Ethernet Interface
Ethernet Interface
Segments
Data
Packets
Frames
Bits (1010001)

## Slide 34: What is transport layer?
Problem: How to turn this host-to-host packet delivery service into a process-to-process communication channel?
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 35: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 36: TCP Three-way Handshake
Timeline for three-way handshake algorithm
The idea is to tell each other
The ISNs
SYN → Client tells server that
it wants to open a connection,
Client’s ISN = x SYN+ ACK → Server tells
Client → Okay → Server’s ISN = y, ACK = CLSeq + 1 Why increment by 1?

## Slide 37: TCP/IP Layers
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Ethernet Interface
Ethernet Interface
Segments
Data
Packets
Frames
Bits (1010001)

## Slide 38: Client-server architecture
server:
always-on host
permanent IP address
data centers for scaling
clients:
communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
client/server
Notes: 38

## Slide 39: Securing Data - Application Layer Function
TCP & UDP
no encryption
cleartext passwds sent into socket traverse Internet in cleartext
SSL
provides encrypted TCP connection
data integrity
end-point authentication
SSL is at app layer
Apps use SSL libraries, which “talk” to TCP
SSL socket API
  cleartext passwds sent into socket traverse Internet encrypted
  More on this later.

## Slide 40: Electronic mail
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP
User Agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Outlook, Thunderbird, iPhone mail client
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent
Notes: 40

## Slide 41: DNS – IP to Name
People: Good with names
Machines: Good with numbers
Ask a person to remember 100s of Ips
- May not work well
DNS maps IP addresses to human readable names.
Notes: 41

## Slide 42: IP Based Communication
google.com
216.58.217.46
google.com
216.58.217.49
GET google.com/index.html
Lookup google.com
Get Data
216.58.217.46
Notes: Mention interest aggregation
Caching

## Slide 43: Summary
- 4 Layers in the network stack
- None of the layers provide security by default
- Security has been always an afterthought
- What are the implications?
- Reading: - Network Security: Private Communication in a Public World
- Chapter 1.8
Notes: 43